## Slide 1
Lyophilized sediment sample
split in three parts (100 mg each)
Control treatment
Reduction treatment
Initial sediment sample
Acid fumigated
Analyzed on CN analyzer
Buffer solution added
(0.27 M trisodium citrate)
Buffer solution added
(1.6 M sodium chloride)
Heated to 80ºC
sodium dithionite added
Sodium chloride added
Kept at 80ºC for 15 minutes
Centrifuged
Supernatant discarded
Artificial lake water added
Vortexed to resuspend pellet
Centrifuged
Supernatant discarded
Dried
Fe-OC extraction step
performed 3x
Rinsing step
performed 3x
Calculations